## Slide 2: I-IoT Low Power Embedded Communication Project: Smart Waste Management
Gregory Gonzalez Lopez
Mouhcine Oulad Ali
Wesley Van Wijnsberghe

## Slide 3: What is Smart Waste Management?
Smart garbage bin
Measure temperature + capacity inside
Transmission of data and its location is triggered by movement of lid
Receive email alert if capacity has reached critical level (IFTTT)
Indoor: d7 + fingerprinting (x,y)
Outdoor: LoRa + GPS (latitude, longitude)

## Slide 4: Overview

## Slide 5: C-code Algorithm
Power on
Initialize sensors
Initialize interrupt accelerometer
Loop:
    active:
    - Read sensor values
      Send using D7
       error: send using LoRa
      Go inactive
  - inactive:
  - periodic wakeup: 20s (demo purposes)
  - if interrupt  go active next wakeup

## Slide 6: Ultrasonic sensor
MOSFET:
  Turn on sensor before measurement
  Turn off once measurement is done

## Slide 7: Outdoor-localization (GPS)
I²C (read & write registers)
NMEA-sentence
    $GNRMC,105824.000,A,5110.577055,N,00420.844651,E,0.42,285.58,080119,,,A*73
Minmea parser (51.176186,N & 4.347366,E)
Coordinates (latitude,longitude)
  LoRa
    TheThingsNetwork (Riot)
      ThingsBoard (MQTT,python)
Stand-By mode (PMTK-command: $PMTK161,1*28\r\n)
Time
Data valid
Latitude (North)
Longitude (East)
Speed (knots)
Course
(degrees)
Datum
Mode indicator + Checksum

## Slide 8: Outdoor-localization (GPS)

## Slide 9: Outdoor-localization (GPS)

## Slide 10: Backend
Subscription on topic on both a D7 broker & LoRa broker adress
Connection to ThingsBoard
If message received is D7:
  1. Start one thread for data processing
   otherwise sends multiple packets to ThingsBoard
  2. Wait a limited time before localization using mongoDB database
   time to receive packet from all D7 gateways

## Slide 11: Backend
Perform required conversion depending on D7 or LoRa message
    LoRa is first parsed on The Things Network using a custom payload decoder
       Decoder supports IFTTT trigger
Send telemetry to ThingsBoard for visualization
  Indoor: map classroom
  Outdoor: Google maps
  Distance & Temperature
  Container level

## Slide 12: Power Management
Send LoRa if D7 failed to send = less airtime
Send coördinates only by LoRa = less payload
Mosfet to turn on ultrasonic if measurement required
Only wakeup active if (x,y,z) movement during sleep interval
Improvements:
Low power mode GPS
Check if indoor or outdoor  no gps measurements/no D7
Ultrasonic sensor draws a lot of current (15mA) = not ideal
Don’t sent accelerometer values = useless